#### 1985 Cessna 182R – N9873E

# Preflight Cabin

- AIF Front cover………….Inspect for Airworthiness

- Pilot’s Operating Handbook Available

- Parking Brake	Set

- Hobbs & Tach	Check

- Fire Extinguisher	Serviceable

- Documents	AROW in airplane

- Control/Avionics Lock	Remove

- Avionics Power Switch	Off

- Ignition Switch	Off

- Master Switch	On

- Flaps	Full Down

- Fuel Quantity Indicators	Check Quantity

- Low-Vacuum Warning Light	Check On

- Avionics Power Switch	On

- Avionics Cooling Fan	.Check Audibly

- Avionics Power Switch	Off

- Pitot Heat 	Check

- Lights	Check

- Master Switch	Off

- Alternate Static	Off

- Fuel Selector	Both

Preflight Empennage

- Baggage Door	.Check for security and lock

- Rudder Gust Lock	Remove

- Tail Tie-Down	Disconnect

- Remove before flight streamer…………………...Remove

- Control Surfaces	Check

Preflight Right Wing trailing edge

- Right Flap	Check

- Right Aileron	Check

- Right Wingtip & Light	Check

# Preflight Right Wing

- Wing Tie Down	Disconnect

- Right Fuel Vent	Check Clear

- Right Main Wheel Tire & Brake	Check

- Right Fuel Sump(s)	Drain

- Right Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure, vent unobstructed

Nose

- Static Sources	Check (Both sides)

- Prop & Spinner	Check

- Landing Lights	Check

- Carburetor Air Filter	Check

- Nose Wheel, Strut & Tire	Check

- Nose Tie-Down	Disconnect

- Engine Oil Dipstick	9-12 Quarts

- Engine Oil Filler Cap	Check Secure

- Fuel Strainer Drain Knob	Pullout to Drain

- Windscreen	Check/Clean

# Preflight Left Wing

- Left Main Wheel Tire & Brake.	Check

- Left Fuel Sump(s)	Drain

- Left Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure

# Preflight Left Wing Leading Edge

- Pitot Tube Cover	Remove

- Left Fuel Vent	Check Clear

- Stall Warning……..Check Operation

- Wing Tie-Down	Disconnect

- Left Wingtip & Light	Check

# Preflight Left Wing Trailing Edge

- Left Aileron	Check

- Left Flap	Check

Before Starting Engine

- Preflight Inspection	Complete

- Passenger Brief	Complete

##### PASSENGER BRIEF

- Seat Belts / Shoulder Harness

- Personal Electronic Devices off

- Air Vents / Comfort

- Fire Extinguisher Location / Operation

- Emergency Procedures & Exits

##### MISSION BRIEF

- Mission Objective

- Destination, WX, Route, Alt, ETE

- NOTAMS

- Crew Coordination & CRM

- Sterile Cockpit Procedures

- Cockpit Layout

- Intercom & Radio Usage

- Seats, Seatbelts, Doors

- Emergency Action & Equipment

Starting Engine

1.  Seats / Belts / Shoulder Harness	Adjust and Lock

2.  Brakes	Test & Set

3.  Fuel Selector Valve…..….…On Both

4.  Elevator/Rudder Trim.............Set for

Takeoff

5.  Cowl Flaps……………………..Open

6.  Mixture…………………………...Rich

7.  Propeller…………………..High RPM

8.   Throttle……….…3 Strokes to prime

then Open 3/8 Inch

9.   Carburetor  Heat……………….Cold

10.  Autopilot………………………..Off

11. Beacon………..………………...On

12. Circuit Breakers……………Check In

13. Primer…………….…In and locked

14. Master Switch…….…..….Both On

15. Propeller Area………….….. .Clear

16. Avionics Power Switch…………..	Off

Caution

The avionics power switch must be OFF during engine start to prevent possible damage to avionics.

17. Ignition Switch………………….Start

Note If engine has been over primed, start with throttle ¼ to ½ open.  Reduce throttle to idle when engine fires.

18.  Starter	Check Disengaged

19.  Throttle	800 to 1000 RPM

20.  Oil Pressure	Check

21.  Avionics Power Switch	On

22.  Nav Lights	On

23.  Taxi Lights	As Required

24.  Flaps	Up

25.  Transponder	TEST/STBY

26.  ATIS / AWOS	Copy

27.  Altimeter	 Set (Verify Within 75’ of

Fld. Elev.)

28.  Clearance Delivery/Ground

Control…………………....Contact

Taxi

- Brakes………….Test (Pilot/Co-Pilot)

- Heat / Vents / Defrost	As Required

- Attitude Indicator	Verify Proper Operation

- Turn Coordinator	Verify Proper Operation

- H.I. & Compass	Verify Proper Operation

- Fuel Selector Valve	Check set to Both

- Engine……………………….… Lean

Before Takeoff - Run-Up

- Parking Brake	Set

- Seats / Belts / Shoulder Harness	Check Secure

- Cabin Doors	Closed and Locked

- Flight Controls	Free & Correct

- Flight Instruments & H.I..	Check & Set

6.  Heading Indicator (H.I.).	To Compass

Caution

The directional indicator should be rechecked during engine run-up to avoid compass deviation errors, which may occur below 1200 RPM.

7.  Fuel Quantity	Check

8.  Selector Valve	Recheck Both

9.  Elevator & Rudder Trim	Set for

Takeoff

10. Cowl Flaps	Recheck Open

11. Mixture…………………………Rich

12. Throttle	1700 RPM

13. Magnetos	Max Drop 150 RPM

14. Carb Heat	Check for RPM Drop

Then Cold

15. Propeller	Cycle

16. Suction Gauge	Check

17. Engine Inst & Ammeter	Check

18. Throttle 	Idle Check, then 800 to

1000 RPM

19.  Primer	In & Locked

20.  Throttle Friction Lock	Adjust

21. Strobe Lights/Pulse Lights

(If installed)	As Desired

22. Radios / Transponder	Set

23. Autopilot (If Installed)	Off

24. Flaps set for Takeoff	0°-20°

25. Electric Trim (If Installed)	Test

26. Takeoff Briefing	Complete

27. Doors & Windows	Latched

28. Lights	Set

29. Transponder	Set to ALT

30. Time	Record

31. Parking Brake	Release

Takeoff

- Flaps	0°-20°

- Carb Heat	Cold

- Power	Full Throttle and 2400 RPM

- Mixture	Full Rich or Max Power

- Engine Instruments	In Green

- Rotate	50 KIAS

- Normal Climb Speed	80 KIAS

- Short Field T.O.	20° Flaps / 57 KIAS Until Clear

- Soft Field T.O	20° Flaps / Ground Effect ASAP

6.  Flaps	Retract (above 70 KIAS)

Enroute Climb

- Airspeed	85-95 KIAS Normal

- Throttle	…23 Inches or Full (whichever is less)

- Propeller	2400 RPM

- Fuel Selector	Both

- Mixture	Full Rich or Max Power

- Cowl Flaps	Open as required

- Engine Instruments	Check

Cruise

- Power	15-23 Inches & 2100-2400 RPM (no more than 75% power).

- Elevator & Rudder Trim	Adjust

- Mixture	Lean

- Cowl Flaps	Closed or as required

- Engine Instruments / Fuel	Check

- Heading Indicator (H.I.).	To Compass

- Lights	As Required

- Flight Plan	Activate as Required

Descent

- Heading Indicator.	To Compass

- Altimeter	Set

- Fuel Selector	Both

- Lights	As Required

- Engine Instruments	Check

- Mixture	Enrich as required

- Power / Carb Heat	As Required

- Cowl Flaps	Closed

- Wing Flaps	As Desired

Before Landing Harness	Secure

- Seat, Seat Belts, Shoulder Harness 	Adjust and Lock

- Fuel Selector	Both

- Mixture	Rich

- Propeller	High RPM

- Carb Heat	On

- Autopilot (If installed)	Off

- Airspeed	70-80 KIAS  (Flaps Up)

- Airspeed	60-70 KIAS (Flaps Down)

- Trim	Adjust

10.Touchdown	Main Wheel First

11. Landing Roll	Lower Nose Wheel Gently

## 12. Braking	Minimum required

## Short Field Landing

- Airspeed	70-80 KIAS  (Flaps Up)

- Flaps	40º (below 95 KIAS)

- Airspeed	Maintain 60 KIAS

- Trim	Adjust

- Power	Reduce to idle as obstacle

is cleared

- Touchdown	Main Wheels First

- Brakes	Apply Heavily

- Flaps	Retract for Max brake effectiveness.

## Balked Landing

- Power	Full Throttle  & 2400 RPM

- Carb Heat	Cold

- Flaps	Retract to 20°

- Climb Speed	55 KIAS

- Flaps	Retract Slowly (above 70 KIAS)

- Cowl Flaps	Open

After Landing (Clear of Runway)

- Flaps	Up

- Carb Heat	Cold

- Cowl Flaps	Open

- Lights	As Required

- Transponder	STBY & 1200

- Mixture	Lean

- Pitot Heat	Off

# Securing Aircraft

- Parking Brake	Set

- Throttle…………………………..Idle

- Magnetos	Check for Ground

- Throttle…….1700 RPM for 15 sec. then back to Idle along with Mixture to Idle cutoff.

- Avionics power & switches…….Off

- Ignition	Off

- Master switch……………………Off

- Control/Avionics Lock	Install

- Parking Brake 	 Off

- Cowl Flaps 	Closed

- Fuel Selector	Left or Right

- Hobbs & Tach	Record

- Pitot Cover…………………..Install

- Tail tie down Remove before flight

Streamer ……………………Install

- Aircraft.	.Secured & Locked

- Flight Plan.	Closed

# V Speeds and Specs

- X-Wind (Max Demo’d)	15 Knots

- Vr  Rotation Speed	50 KIAS

- Vx  Best Angle Climb	57 KIAS

- Vy  Best Rate Climb	78 KIAS

- Vso  Stall w/ Flaps	45 KIAS

- Vs1  Stall w/o Flaps	48 KIAS

- Best Glide	70 KIAS

- Va  Max Abrupt Ctrl (2950 Lbs)	111 KIAS

- Va  Max Abrupt Ctrl (2450 Lbs)	100 KIAS

- Va Max Abrupt Ctrl (1950 Lbs)	89 KIAS

- Vno  Max Structural Cruise	143 KIAS

- Vne  Never Exceed	179 KIAS

- Vfe  10° Flaps	140 KIAS

- Vfe  10°-Full Flaps	95 KIAS

General...

- EMERGENCY	121.50

- Unicom	122.70-122.80-122.95

123.00-123.05

- Multicom	122.90 (CTAF)

- Flight Service	122.20 (Most Common) 122.10-122.60-123.60

- Flight Watch	122.00

- Air to Air	122.75-122.85-123.45

Transponder Codes

- 1200	VFR

- 7500	HIJACK

- 7600	LOST COMMS

- 7700	EMERGENCY

# Aircraft Information

- Gross Weight Capacity

2950 (Takeoff)	2950 (Landing)

- Engine	Continental O-470-U

- Max Power	230 BHP

- Fuel Type	100LL (Blue)

- Fuel Capacity (Standard)	88 Gal Usable

- Oil Type	Exxon Elite 15W-50

- Oil Capacity	12 Qts (Minimum 9)

- Electrical	24-28 Volt / 60 Amp

- Tire Pressure	Nose-49 PSI / Main-42 PSI

This checklist is a guide to coordinate Pilot Operating Handbook and STC data applicable to this particular aircraft only.  The applicable Pilot Operating Handbook and STC installations remain the official documentation for this aircraft.

The pilot in command is responsible for complying with all items in the Pilot Operating Handbook and applicable STCs.

I certify this checklist has been reviewed for accuracy.

_Michael J Mueller, 2 February 2010

_____________________________________

Wing Director of Maintenance              Date

# Text boxes

Warning

When turning on the master switch, using an external power source, or pulling the propeller through by hand, treat the propeller as if the ignition switch were on.  Do not stand, nor allow anyone else to stand, within the arc of the propeller, since a loose or broken wire, or a component malfunction, could cause the propeller to rotate.