#### 1985 Cessna 172P – N98914

Air Plains 180 HP Conversion

# Preflight Cabin

- AIF Front Cover…………Inspect for Airworthiness

- Pilot’s Operating Handbook Available

- Parking Brake	Set

- Hobbs & Tach	Check

- Fire Extinguisher	Serviceable

- Documents	AROW in airplane

- Control/Avionics Lock	Remove

- Ignition Switch	Off

- Avionics Power Switch	Off

- Master Switch	On

- Wing Flaps	30º

- Fuel Quantity Indicators	Check Quantity

- Avionics Cooling Fan	..Check Audibly for Operation

- Pitot Heat 	Check As Required

- Lights	Check

- Master Switch	Off

- Static Pressure Alternate Source Valve (if installed)	Off

- Fuel Selector	Both

Preflight Empennage

- Baggage Door	.Check for security and lock

- Rudder Gust Lock	Remove

- Tail Tie-Down	Disconnect

- Control Surfaces	Check

Preflight Right Wing trailing edge

- Right Flap	Check

- Right Aileron	Check

- Right Wingtip & Light	Check

# Preflight Right Wing

- Wing Tie Down	Disconnect

- Right Main Wheel Tire & Brake	Check

- Right Fuel Sump	Drain

- Fuel Selector Quick-Drain Valve	Drain

- Right Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure, vent unobstructed

Nose

- Static Source	Check (Left side)

- Prop & Spinner	Check

- Landing Lights	Check

- Carburetor Air Filter	Check

- Nose Wheel, Strut & Tire	Check

- Nose Tie-Down	Disconnect

- Engine Oil Filler Cap	Check Secure

- Engine Oil Dipstick	5-7 Quarts (7 for extended flights)

- Fuel Strainer Drain Knob	Pullout to Drain

- Windscreen	Check/Clean

# Preflight Left Wing

- Left Main Wheel Tire & Brake	Check

- Left Fuel Sump	Drain

- Left Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure

# Preflight Left Wing Leading Edge

- Pitot Tube Cover	Remove

- Left Fuel Vent	Check Clear

- Stall Warning	Check

- Wing Tie-Down	Disconnect

- Left Wingtip & Light	Check

# Preflight Left Wing Trailing Edge

- Left Aileron	Check

- Left Flap	Check

##### PASSENGER BRIEF

- Seat Belts / Shoulder Harness

- Personal Electronic Devices off

- Air Vents / Comfort

- Fire Extinguisher Location / Operation

- Emergency Procedures & Exits

##### MISSION BRIEF

- Mission Objective

- Destination, WX, Route, Alt, ETE

- NOTAMS

- Crew Coordination & CRM

- Sterile Cockpit Procedures

- Cockpit Layout

- Intercom & Radio Usage

- Seats, Seatbelts, Doors

- Emergency Action & Equipment

Before Starting Engine

- Preflight Inspection	Complete

- Passenger Brief	Complete

- Seats / Belts / Shoulder Harness	Adjust and Lock

- Fuel Selector Valve	Both

- Avionics Power Switch	Off

Caution

The avionics power switch must be OFF during engine start to prevent possible damage to avionics.

- Autopilot (If Installed)	Off

- Electrical Equipment	Off

- Brakes	Test & Set

- Circuit Breakers	Check In

# Starting Engine

- Mixture	Rich

- Carburetor Heat	Cold

- Master Switch	On

- Prime	As Required (2 to 6 strokes)

- Throttle	Open 1/8 Inch

- Propeller Area	Clear

- Ignition Switch	Start

- Throttle	800 to 1000 RPM

- Oil Pressure	Check

- Starter	Check Disengaged

- Flashing Beacon & Nav Lights	On

- Avionics Power Switch	On

- Radios	On

- Taxi Lights	As Required

- Flaps	Up

- Transponder	TEST/STBY

- ATIS / AWOS	Copy

- Altimeter	 Set (Verify Within 75’ of Fld Elev.)

- Clearance Delivery/Ground Control	Contact

Taxi

- Brakes	Test

- Heat / Vents / Defrost	As Required

- Attitude Indicator	Verify Proper Operation

- Turn Coordinator	Verify Proper Operation

- H.I. & Compass	Verify Proper Operation

- Fuel Selector Valve	Check & Set to Both

Before Takeoff - Run-Up

- Parking Brake	Set

- Seats / Belts / Shoulder Harness	Check Secure

- Cabin Doors & Windows..	Closed and Locked

- Flight Controls	Free & Correct

- Flight Instruments & H.I.	.Check & Set

- Fuel Quantity	Check

- Mixture	Rich

- Fuel Selector Valve	Recheck Both

- Elevator & Rudder Trim	Set for Takeoff

- Throttle	1700 RPM

- Magnetos..Max Drop 125 RPM - 50 RPM differential

- Carb Heat	Check for RPM Drop

- Suction Gauge	Check

- Engine Inst & Ammeter	Check

- Throttle	Idle Check, then 800 to 1000 RPM

- Throttle Friction Lock	Adjust

- Strobe Lights/Pulse Lights

(If installed)	As Desired

- Radios / Transponder	Set

- Autopilot (If Installed)	Off

- Flaps set for Takeoff	0°-10°

- Primer	In & Locked

- Carb Heat	Cold

- Takeoff Briefing	Complete

- Doors & Windows	Latched

- Lights	Set

- Transponder	Set to ALT

- Time	Record

- Parking Brake	Release

Takeoff

- Flaps	0°-10°

- Carb Heat	Cold

- Throttle	Full Open

- Mixture	Full Rich or Max Power

- Engine Instruments	In Green

- Rotate	55 KIAS

- Climb Speed	75 to 85 KIAS

- Short Field T.O.	..10° Flaps / 57 KIAS Until Clear

- Soft Field T.O…	10° Flaps / Ground Effect ASAP

6.  Wing Flaps	..Retract (above 70 KIAS)

Enroute Climb

- Airspeed	75 - 85 KIAS Normal

Note

If a maximum performance climb is necessary, use speeds shown in the Rate Of Climb chart in POH Section 5.

- Throttle	Full Open

- Fuel Selector	Both

- Mixture	Full Rich or Max RPM

- Engine Instruments	Check

Cruise

- Power	2100-2700 RPM (no more than 75% is recommended)

- Elevator & Rudder Trim	Adjust

- Mixture	Lean

- Engine Instruments / Fuel	Check

- Heading Indicator (H.I.).	To Compass

- Lights	As Required

- Flight Plan	Activate as Required

Descent

- Heading Indicator.	To Compass

- Altimeter	Set

- Fuel Selector	Both

- Lights	As Required

- Engine Instruments	Check

- Mixture	…Adjust for Smooth Operation (full rich for idle power)

- Carb Heat	Full Heat as Required

Before LandingHarness	Secure

- Seat, Seat Belts, Shoulder Harness 	Secure

- Fuel Selector Valve	Both

- Mixture	Rich

- Carb Heat	..On (Apply Full Heat Before Closing Throttle)

- Autopilot (If installed)	Off

- Airspeed	65-75 KIAS  (Flaps Up)

- Wing Flaps	As Desired (Below 85 KIAS)(Maximum Flap Travel is 30º)

- Airspeed	60-70 KIAS (Flaps Down)

- Trim	Adjust

10.Touchdown	Main Wheel First

11. Landing Roll	Lower Nose Wheel Gently

## 12. Braking	Minimum required

## Short Field Landing

- Airspeed	65-75 KIAS  (Flaps Up)

- Wing Flaps	30º (below 85 KIAS)

- Airspeed	Maintain 62 KIAS (Until Flare)

- Trim	Adjust

Power….	Reduce to idle after clearing obstacle

- Touchdown	Main Wheels First

- Brakes	Apply Heavily

- Wing Flaps	Retract

## Balked Landing

- Throttle	Full Open

- Carb Heat	Cold

- Wing Flaps	20° (Immediately)

- Climb Speed	60 KIAS

- Wing Flaps	…10º (Until Obstacles are Cleared)

- Wing Flaps….	Retract (After reaching a safe altitude and 65 KIAS)

After Landing (Clear of Runway)

- Wing Flaps	Up

- Carb Heat	Cold

- Lights	As Required

- Transponder	STBY & 1200

- Mixture	Lean

- Pitot Heat	Off

# Securing Aircraft

- Parking Brake	Set

- Throttle	Idle

- Avionics Power & Switches	Off

- Magnetos	Check for Ground

- Mixture	Idle Cut Off

- Ignition & Master Switch	Off

- Control/Avionics Lock	Install

- Parking Brake 	 Off

- Fuel Selector	Left or Right

- Hobbs & Tach	Record

- Aircraft	Secured & Locked

- Flight Plan	Closed

# V Speeds and Specs

- X-Wind (Max Demo’d)	15 Knots

- Vr  Rotation Speed	55 KIAS

- Vx  Best Angle Climb	62 KIAS

- Vy  Best Rate Climb	76 KIAS

- Vso  Stall w/ Flaps	40 KIAS

- Vs1  Stall w/o Flaps	50 KIAS

- Best Glide (2300 Lbs)	65 KIAS

- Va  Max Abrupt Ctrl (2550 Lbs)	105 KIAS

- Va  Max Abrupt Ctrl (2150 Lbs)	95 KIAS

- Va Max Abrupt Ctrl (1750 Lbs)	85 KIAS

- Vno  Max Structural Cruise	..127 KIAS

- Vne  Never Exceed	158 KIAS

- Vfe  10°-Full Flaps	85 KIAS

- Max Window Open Speed	…158 KIAS

V Speeds and Specs are based on sea level. Consult the Air Plains Services, Corp. FAA Approved Airplane Flight Manual Supplement for V speed and Specs for operations above sea level.

General...

- EMERGENCY	121.50

- Unicom	122.70-122.80-122.95

123.00-123.05

- Multicom	122.90 (CTAF)

- Flight Service	122.20 (Most Common) 122.10-122.60-123.60

- Flight Watch	122.00

- Air to Air	122.75-122.85-123.45

Transponder Codes

- 1200	VFR

- 7500	HIJACK

- 7600	LOST COMMS

- 7700	EMERGENCY

# Aircraft Information

- Gross Weight Capacity

2550 (Takeoff)	2550 (Landing)

- Engine	Lycoming  O-360-A4M

- Max Power	180 BHP

- Max Engine Speed	2700 RPM

- Fuel Type	100LL (Blue)

- Fuel Capacity (Standard)	40 Gal Usable

- Fuel Capacity (Long Range).	50 Gal Usable

- Oil Type	SAE 50

- Oil Capacity	7 Qts (Minimum 5)

- Electrical	24 - 28 Volt / 60 Amp

- Tire Pressure	Nose-45 PSI / Main-38 PSI

This checklist is a guide to coordinate Pilot Operating Handbook and STC data applicable to this particular aircraft only.  The applicable Pilot Operating Handbook and STC installations remain the official documentation for this aircraft.

The pilot in command is responsible for complying with all items in the Pilot Operating Handbook and applicable STCs.

I certify this checklist has been reviewed for accuracy.

Michael J Mueller, 2 February 2010

______________________________________

Wing Director of Maintenance              Date

# Text boxes

Warning

When turning on the master switch, using an external power source, or pulling the propeller through by hand, treat the propeller as if the ignition switch were on.  Do not stand, nor allow anyone else to stand, within the arc of the propeller, since a loose or broken wire, or a component malfunction, could cause the propeller to rotate.